## Slide 1
인터페이스명세서(검사기)
관리부서 : 화학담당
Copyright © LG CNS. LG CNS의 사전 승인 없이 본 내용의 전부 또는 일부에 대한 복사, 전재, 배포, 사용을 금합니다.
LGCWA MES 구축
문서번호 : LGC-설계-인터페이스명세서(검사기)-LGCWA 모듈21호

## Slide 2
3. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
3.1. 제어 항목(HIPOT)
제품ID | 공정ID | 제어항목ID | 제어항목명 | 제어값 | 단위
AMDAU0149B | P4200 | WP2MMMTC1001 | (+)_Bushing Isolation Resistance Test Voltage Level | 500 | V
AMDAU0149B | P4200 | WP2MMMTC1002 | (+)_Bushing Isolation Resistance Test Voltage Time | 60 | Sec
AMDAU0149B | P4200 | WP2MMMTC1003 | (+)_Cooling Plate Isolation Resistance Test Voltage Level | 500 | V
AMDAU0149B | P4200 | WP2MMMTC1004 | (+)_Cooling Plate Isolation Resistance Test Voltage Time | 60 | Sec
AMDAU0149B | P4200 | WP2MMMTC1005 | (-)_Bushing Isolation Resistance Test Voltage Level | 500 | V
AMDAU0149B | P4200 | WP2MMMTC1006 | (-)_Bushing Isolation Resistance Test Voltage Time | 60 | Sec
AMDAU0149B | P4200 | WP2MMMTC1007 | (-)_Cooling Plate Isolation Resistance Test Voltage Level | 500 | V
AMDAU0149B | P4200 | WP2MMMTC1008 | (-)_Cooling Plate Isolation Resistance Test Voltage Time | 60 | Sec
AMDAU0149B | P4200 | WP2MMMTC1009 | Hi pot Current Range | 0.000003 | A
제품코드 : AMDAU0149B
공정 ID : P4200
설비 ID : W1PCMA214-7-5, W1PCMA214-7-6, W1PCMA214-7-7
미사용 요청

## Slide 3
3. CWA 모듈 12호기 CMA 충/방전 검사장비 I/F
3.2. 제어 항목(DCIR)
제품ID | 공정ID | 제어항목ID | 제어항목명 | 제어값 | 단위
AMDAU0149B | P4000 | WP2MMMTC2001 | Cell Line Open Check Upper Limit | 750 | kΩ
AMDAU0149B | P4000 | WP2MMMTC2002 | Cell Line Open Check Lower Limit | 650 | kΩ
AMDAU0149B | P4000 | WP2MMMTC2003 | Rest Time before discharge | 3 | Sec
AMDAU0149B | P4000 | WP2MMMTC2004 | Discharge Current | 120 | A
AMDAU0149B | P4000 | WP2MMMTC2005 | Discharge Time | 10 | Sec
AMDAU0149B | P4000 | WP2MMMTC2006 | Discharge Current Upper Limit | 125 | A
AMDAU0149B | P4000 | WP2MMMTC2007 | Rest Time after discharge | 30 | Sec
AMDAU0149B | P4000 | WP2MMMTC2008 | Charge Current | 120 | A
AMDAU0149B | P4000 | WP2MMMTC2009 | Charge Time | 10 | Sec
AMDAU0149B | P4000 | WP2MMMTC2010 | Charge Current Upper Limit | 125 | A
AMDAU0149B | P4000 | WP2MMMTC2011 | Rest Time after charge | 1 | Sec
AMDAU0149B | P4000 | WP2MMMTC2012 | Safety Voltage Upper Limit | 50.4 | V
AMDAU0149B | P4000 | WP2MMMTC2013 | Safety Voltage Lower Limit | 36 | V
AMDAU0149B | P4000 | WP2MMMTC2014 | Cell DCIR 온도보정식 계수1 | 0.155 | 
AMDAU0149B | P4000 | WP2MMMTC2015 | Cell DCIR 온도보정식 계수2 | 0 | 
AMDAU0149B | P4000 | WP2MMMTC2016 | Module DCIR 온도보정식 계수1 | 1.68 | 
AMDAU0149B | P4000 | WP2MMMTC2017 | Module DCIR 온도보정식 계수2 | 0 | 
AMDAU0149B | P4000 | WP2MMMTC2018 | Cell DCIR 온도보정식 계수3 | 0.0022 | 
AMDAU0149B | P4000 | WP2MMMTC2019 | Module DCIR 온도보정식 계수3 | 0.0264 | 
AMDAU0149B | P4000 | WP2MMMTC2020 | Stacking sequence (normal =0, reverse =1) | 1 | 
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10

## Slide 4
제품ID` | 공정ID | 수집항목ID | 수집항목명 | LSL | USL | 단위 | 비고 | 불량코드
AMDAU0149B | P4200 | WP2MMMTQ1001 | Probe Contact Check Bushing | 20 | 200 | nF |  | 
AMDAU0149B | P4200 | WP2MMMTQ1002 | Probe Contact Check Cooling Plate | 20 | 200 | nF |  | 
AMDAU0149B | P4200 | WP2MMMTQ1003 | Insulation Resistacne (+)~Bushing | 40 | 999999 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1004 | Insulation Resistacne (+)~Cooling plate | 40 | 999999 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1005 | Insulation Resistacne (-)~Bushing | 40 | 999999 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1006 | Insulation Resistacne (-)~Cooling plate | 40 | 999999 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1007 | Probe Contact Check Bushing2 | 20 | 200 | nF |  | 
AMDAU0149B | P4200 | WP2MMMTQ1008 | Probe Contact Check Cooling Plate2 | 20 | 200 | nF |  | 
4. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
4.1. 수집 항목(HIPOT)
제품코드 : AMDAU0149B
공정 ID : P4200
설비 ID : W1PCMA214-7-5, W1PCMA214-7-6, W1PCMA214-7-7
미사용 요청

## Slide 5
제품ID` | 공정ID | 수집항목ID | 수집항목명 | LSL | USL | 단위 | 비고 | 불량코드
AMDAU0149B | P4200 | WP2MMMTQ1009 | Probe Contact Check Bushing - Control limit | 20 | 200 | nF |  | 
AMDAU0149B | P4200 | WP2MMMTQ1010 | Probe Contact Check Cooling Plate - Control limit | 20 | 200 | nF |  | 
AMDAU0149B | P4200 | WP2MMMTQ1011 | Insulation Resistacne (+)~Bushing - Control limit | 800 | 999999 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1012 | Insulation Resistacne (+)~Cooling plate - Control limit | 800 | 10000 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1013 | Insulation Resistacne (-)~Bushing - Control limit | 40 | 999999 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1014 | Insulation Resistacne (-)~Cooling plate - Control limit | 40 | 999999 | MΩ |  | 
AMDAU0149B | P4200 | WP2MMMTQ1015 | Probe Contact Check Bushing2 - Control limit | 20 | 200 | nF |  | 
AMDAU0149B | P4200 | WP2MMMTQ1016 | Probe Contact Check Cooling Plate2 - Control limit | 20 | 200 | nF |  | 
4. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
4.1. 수집 항목(HIPOT)
제품코드 : AMDAU0149B
공정 ID : P4200
설비 ID : W1PCMA214-7-5, W1PCMA214-7-6, W1PCMA214-7-7

## Slide 6
제품ID | 공정ID | 수집항목ID | 수집항목명 | LSL | USL | 단위 | 비고 | 불량코드
AMDAU0149B | P4000 | WP2MMMTQ2001 | Temperature Deviation | -5.0 | 5.0 | ℃ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2002 | Cell Voltage 1 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2003 | Cell Voltage 2 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2004 | Cell Voltage 3 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2005 | Cell Voltage 4 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2006 | Cell Voltage 5 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2007 | Cell Voltage 6 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2008 | Cell Voltage 7 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2009 | Cell Voltage 8 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2010 | Cell Voltage 9 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2011 | Cell Voltage 10 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2012 | Cell Voltage 11 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2013 | Cell Voltage 12 | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2014 | Cell Voltage deviation | 0 | 40 | mV |  | 
AMDAU0149B | P4000 | WP2MMMTQ2015 | Module Voltage | 41.878 | 42.362 | V |  | 
4. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
4.2. 수집 항목(DCIR)
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10

## Slide 7
제품ID | 공정ID | 수집항목ID | 수집항목명 | LSL | USL | 단위 | 비고 | 불량코드
AMDAU0149B | P4000 | WP2MMMTQ2016 | Cell DCIR 1 | 0 | 1.739 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2017 | Cell DCIR 2 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2018 | Cell DCIR 3 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2019 | Cell DCIR 4 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2020 | Cell DCIR 5 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2021 | Cell DCIR 6 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2022 | Cell DCIR 7 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2023 | Cell DCIR 8 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2024 | Cell DCIR 9 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2025 | Cell DCIR 10 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2026 | Cell DCIR 11 | 0 | 1.756 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2027 | Cell DCIR 12 | 0 | 1.745 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2028 | Cell DCIR Deviation | 0 | 0.665 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2029 | Cell DCIR Ratio | 100 | 164 | % |  | 
AMDAU0149B | P4000 | WP2MMMTQ2030 | Module DCIR | 0 | 20.621 | mΩ |  | 
4. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
4.2. 수집 항목(DCIR)
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10

## Slide 8
제품ID | 공정ID | 수집항목ID | 수집항목명 | LSL | USL | 단위 | 비고 | 불량코드
AMDAU0149B | P4000 | WP2MMMTQ2031 | Temperature Deviation - Control limit | -3 | 3 | ℃ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2032 | Cell Voltage 1 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2033 | Cell Voltage 2 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2034 | Cell Voltage 3 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2035 | Cell Voltage 4 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2036 | Cell Voltage 5 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2037 | Cell Voltage 6 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2038 | Cell Voltage 7 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2039 | Cell Voltage 8 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2040 | Cell Voltage 9 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2041 | Cell Voltage 10 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2042 | Cell Voltage 11 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2043 | Cell Voltage 12 - Control limit | 3.490 | 3.530 | V |  | 
AMDAU0149B | P4000 | WP2MMMTQ2044 | Cell Voltage deviation - Control limit | 0 | 18 | mV |  | 
AMDAU0149B | P4000 | WP2MMMTQ2045 | Module Voltage - Control limit | 41.878 | 42.362 | V |  | 
4. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
4.2. 수집 항목(DCIR)
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10

## Slide 9
제품ID | 공정ID | 수집항목ID | 수집항목명 | LSL | USL | 단위 | 비고 | 불량코드
AMDAU0149B | P4000 | WP2MMMTQ2046 | Cell DCIR 1 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2047 | Cell DCIR 2 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2048 | Cell DCIR 3 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2049 | Cell DCIR 4 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2050 | Cell DCIR 5 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2051 | Cell DCIR 6 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2052 | Cell DCIR 7 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2053 | Cell DCIR 8 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2054 | Cell DCIR 9 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2055 | Cell DCIR 10 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2056 | Cell DCIR 11 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2057 | Cell DCIR 12 - Control limit | 1.3 | 1.71 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2058 | Cell DCIR Deviation - Control limit | 0.00 | 0.28 | mΩ |  | 
AMDAU0149B | P4000 | WP2MMMTQ2059 | Cell DCIR Ratio - Control limit | 100 | 164 | % |  | 
AMDAU0149B | P4000 | WP2MMMTQ2060 | Module DCIR - Control limit | 16 | 20.621 | mΩ |  | 
4. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
4.2. 수집 항목(DCIR)
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10

## Slide 10
제품ID | 공정ID | 수집항목ID | 수집항목명 | 단위 | 비고
AMDAU0149B | P4200 | WP2MMMTE1001 | (+)_Bushing Isolation Resistance Test Voltage Level | V | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1002 | (+)_Bushing Isolation Resistance Test Voltage Time | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1003 | (+)_Cooling Plate Isolation Resistance Test Voltage Level | V | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1004 | (+)_Cooling Plate Isolation Resistance Test Voltage Time | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1005 | (-)_Bushing Isolation Resistance Test Voltage Level | V | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1006 | (-)_Bushing Isolation Resistance Test Voltage Time | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1007 | (-)_Cooling Plate Isolation Resistance Test Voltage Level | V | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1008 | (-)_Cooling Plate Isolation Resistance Test Voltage Time | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4200 | WP2MMMTE1009 | Insulation Resistacne (+)~Bushing 5s |  | 
AMDAU0149B | P4200 | WP2MMMTE1010 | Insulation Resistacne (+)~Bushing 10s |  | 
AMDAU0149B | P4200 | WP2MMMTE1011 | Insulation Resistacne (+)~Bushing 15s |  | 
AMDAU0149B | P4200 | WP2MMMTE1012 | Insulation Resistacne (+)~Bushing 20s |  | 
AMDAU0149B | P4200 | WP2MMMTE1013 | Insulation Resistacne (+)~Bushing 25s |  | 
AMDAU0149B | P4200 | WP2MMMTE1014 | Insulation Resistacne (+)~Bushing 30s |  | 
AMDAU0149B | P4200 | WP2MMMTE1015 | Insulation Resistacne (+)~Bushing 35s |  | 
AMDAU0149B | P4200 | WP2MMMTE1016 | Insulation Resistacne (+)~Bushing 40s |  | 
AMDAU0149B | P4200 | WP2MMMTE1017 | Insulation Resistacne (+)~Bushing 45s |  | 
AMDAU0149B | P4200 | WP2MMMTE1018 | Insulation Resistacne (+)~Bushing 50s |  | 
AMDAU0149B | P4200 | WP2MMMTE1019 | Insulation Resistacne (+)~Bushing 55s |  | 
AMDAU0149B | P4200 | WP2MMMTE1020 | Insulation Resistacne (+)~Bushing 60s |  | 
5. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
5.1. 상세 수집 항목(HIPOT)
제품코드 : AMDAU0149B
공정 ID : P4200
설비 ID : W1PCMA214-7-5, W1PCMA214-7-6, W1PCMA214-7-7

## Slide 11
제품ID | 공정ID | 수집항목ID | 수집항목명 | 단위 | 비고
AMDAU0149B | P4200 | WP2MMMTE1021 | Insulation Resistacne (+)~Cooling plates 5s |  | 
AMDAU0149B | P4200 | WP2MMMTE1022 | Insulation Resistacne (+)~Cooling plates 10s |  | 
AMDAU0149B | P4200 | WP2MMMTE1023 | Insulation Resistacne (+)~Cooling plates 15s |  | 
AMDAU0149B | P4200 | WP2MMMTE1024 | Insulation Resistacne (+)~Cooling plates 20s |  | 
AMDAU0149B | P4200 | WP2MMMTE1025 | Insulation Resistacne (+)~Cooling plates 25s |  | 
AMDAU0149B | P4200 | WP2MMMTE1026 | Insulation Resistacne (+)~Cooling plates 30s |  | 
AMDAU0149B | P4200 | WP2MMMTE1027 | Insulation Resistacne (+)~Cooling plates 35s |  | 
AMDAU0149B | P4200 | WP2MMMTE1028 | Insulation Resistacne (+)~Cooling plates 40s |  | 
AMDAU0149B | P4200 | WP2MMMTE1029 | Insulation Resistacne (+)~Cooling plates 45s |  | 
AMDAU0149B | P4200 | WP2MMMTE1030 | Insulation Resistacne (+)~Cooling plates 50s |  | 
AMDAU0149B | P4200 | WP2MMMTE1031 | Insulation Resistacne (+)~Cooling plates 55s |  | 
AMDAU0149B | P4200 | WP2MMMTE1032 | Insulation Resistacne (+)~Cooling plates 60s |  | 
AMDAU0149B | P4200 | WP2MMMTE1033 | Ambient Temperature |  | 절연저항 검사 전 측정 외기 온도
AMDAU0149B | P4200 | WP2MMMTE1034 | Insulation Resistacne (-)~Bushing 5s |  | 
AMDAU0149B | P4200 | WP2MMMTE1035 | Insulation Resistacne (-)~Bushing 10s |  | 
AMDAU0149B | P4200 | WP2MMMTE1036 | Insulation Resistacne (-)~Bushing 15s |  | 
AMDAU0149B | P4200 | WP2MMMTE1037 | Insulation Resistacne (-)~Bushing 20s |  | 
AMDAU0149B | P4200 | WP2MMMTE1038 | Insulation Resistacne (-)~Bushing 25s |  | 
AMDAU0149B | P4200 | WP2MMMTE1039 | Insulation Resistacne (-)~Bushing 30s |  | 
AMDAU0149B | P4200 | WP2MMMTE1040 | Insulation Resistacne (-)~Bushing 35s |  | 
AMDAU0149B | P4200 | WP2MMMTE1041 | Insulation Resistacne (-)~Bushing 40s |  | 
AMDAU0149B | P4200 | WP2MMMTE1042 | Insulation Resistacne (-)~Bushing 45s |  | 
AMDAU0149B | P4200 | WP2MMMTE1043 | Insulation Resistacne (-)~Bushing 50s |  | 
AMDAU0149B | P4200 | WP2MMMTE1044 | Insulation Resistacne (-)~Bushing 55s |  | 
5. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
5.1. 상세 수집 항목(HIPOT)
제품코드 : AMDAU0149B
공정 ID : P4200
설비 ID : W1PCMA214-7-5, W1PCMA214-7-6, W1PCMA214-7-7
미사용 요청

## Slide 12
제품ID | 공정ID | 수집항목ID | 수집항목명 | 단위 | 비고
AMDAU0149B | P4200 | WP2MMMTE1045 | Insulation Resistacne (-)~Bushing 60s |  | 
AMDAU0149B | P4200 | WP2MMMTE1046 | Insulation Resistacne (-)~Cooling plates 5s |  | 
AMDAU0149B | P4200 | WP2MMMTE1047 | Insulation Resistacne (-)~Cooling plates 10s |  | 
AMDAU0149B | P4200 | WP2MMMTE1048 | Insulation Resistacne (-)~Cooling plates 15s |  | 
AMDAU0149B | P4200 | WP2MMMTE1049 | Insulation Resistacne (-)~Cooling plates 20s |  | 
AMDAU0149B | P4200 | WP2MMMTE1050 | Insulation Resistacne (-)~Cooling plates 25s |  | 
AMDAU0149B | P4200 | WP2MMMTE1051 | Insulation Resistacne (-)~Cooling plates 30s |  | 
AMDAU0149B | P4200 | WP2MMMTE1052 | Insulation Resistacne (-)~Cooling plates 35s |  | 
AMDAU0149B | P4200 | WP2MMMTE1053 | Insulation Resistacne (-)~Cooling plates 40s |  | 
AMDAU0149B | P4200 | WP2MMMTE1054 | Insulation Resistacne (-)~Cooling plates 45s |  | 
AMDAU0149B | P4200 | WP2MMMTE1055 | Insulation Resistacne (-)~Cooling plates 50s |  | 
AMDAU0149B | P4200 | WP2MMMTE1056 | Insulation Resistacne (-)~Cooling plates 55s |  | 
AMDAU0149B | P4200 | WP2MMMTE1057 | Insulation Resistacne (-)~Cooling plates 60s |  | 
AMDAU0149B | P4200 | WP2MMMTE1057 | Hi pot Current Range |  | 
5. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
5.1. 상세 수집 항목(HIPOT)
제품코드 : AMDAU0149B
공정 ID : P4200
설비 ID : W1PCMA214-7-5, W1PCMA214-7-6, W1PCMA214-7-7

## Slide 13
제품ID | 공정ID | 수집항목ID | 수집항목명 | 단위 | 비고
AMDAU0149B | P4000 | WP2MMMTE2001 | Rest Time before discharge | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2002 | Discharge Current | A | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2003 | Discharge Time | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2004 | Discharge Current Upper Limit | A | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2005 | Rest Time after discharge | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2006 | Charge Current | A | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2007 | Charge Time | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2008 | Charge Current Upper Limit | A | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2009 | Rest Time after charge | Sec | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2010 | Safety Voltage Upper Limit | V | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2011 | Safety Voltage Lower Limit | V | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2012 | Cell DCIR 온도보정식 계수1 |  | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2013 | Cell DCIR 온도보정식 계수2 |  | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2014 | Module DCIR 온도보정식 계수1 |  | 제품 검사 시 적용한 제어값 기록
AMDAU0149B | P4000 | WP2MMMTE2015 | Module DCIR 온도보정식 계수2 |  | 제품 검사 시 적용한 제어값 기록
5. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
5.2. 상세 수집 항목(DCIR)
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10

## Slide 14
제품ID | 공정ID | 수집항목ID | 수집항목명 | 단위 | 비고
AMDAU0149B | P4000 | WP2MMMTE2016 | Ambient Temp | ℃ | 온도 편차 항목에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2017 | Module Temp | ℃ | 온도 편차 항목에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2018 | Max Cell Voltage | V | Cell 전압 편차 항목에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2019 | Min Cell Voltage | V | Cell 전압 편차 항목에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2020 | Ambient Temp before discharge | ℃ | DCIR 직전에 측정된 온도
AMDAU0149B | P4000 | WP2MMMTE2021 | Module Temp before discharge | ℃ | DCIR직전에 측정된 온도
AMDAU0149B | P4000 | WP2MMMTE2022 | Ambient Temp after discharge | ℃ | DCIR직후에 측정된 온도
AMDAU0149B | P4000 | WP2MMMTE2023 | Module Temp after discharge | ℃ | DCIR직후에 측정된 온도
AMDAU0149B | P4000 | WP2MMMTE2024 | Cell Voltage 1~12 before discharge | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2025 | Cell Voltage 1~12 at discharge 10s | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2026 | Cell Voltage 1~12 before charge | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2027 | Cell Voltage 1~12 at charge 10s | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2028 | Cell Voltage 1~12 after charge | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2029 | Max Cell DCIR | mΩ | Cell DCIR 편차/Ratio에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2030 | Min Cell DCIR | mΩ | Cell DCIR 편차/Ratio에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2031 | Module Voltage_Cycler before discharge | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2032 | Module Voltage_Cycler at discharge 10s | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2033 | Module Voltage_Cycler before charge | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2034 | Module Voltage_Cycler at charge 10s | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2035 | Module Voltage_Cycler at rest time after charge | V | DCIR 계산에 적용된 측정값
AMDAU0149B | P4000 | WP2MMMTE2036 | Cell DCIR 온도보정식 계수3 |  | 
AMDAU0149B | P4000 | WP2MMMTE2037 | Module DCIR 온도보정식 계수3 |  | 
5. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
5.2. 상세 수집 항목(DCIR)
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10

## Slide 15
제품ID | 공정ID | 수집항목ID | 수집항목명 | 단위 | 비고
AMDAU0149B | P4000 | WP2MMMTE2038 | Each Cell Voltage deviation( EOL – LQC ) |  | 
AMDAU0149B | P4000 | WP2MMMTE2039 | Stacking sequence |  | (normal =0, reverse =1)
AMDAU0149B | P4000 | WP2MMMTE2040 | Cell Lot ID |  | 
AMDAU0149B | P4000 | WP2MMMTE2041 | Cell Voltage from LQC |  | 
5. CWA 모듈 21호기 CMA 충/방전 검사장비 I/F
5.2. 상세 수집 항목(DCIR)
제품코드 : AMDAU0149B
공정 ID : P4000
설비 ID : W1PCMA214-7-8, W1PCMA214-7-9, W1PCMA214-7-10